## Slide 1: Forecasting Cargo Throughput in Israeli Ports 2018-2048
Sani Ziv, Jonathan Katz, Oren Shapir
November 5, 2018

## Slide 2: Cargo Forecasting Model
The cargo forecasting model was developed in the framework of the strategic development master plan led by the Israel Ports Company.
The model is intended to forecast demand for container cargo, bulk cargo, and general cargo in Israel for the years 2018-2048.

## Slide 3: Project Goal
To forecast the expected volume of goods unloaded and exports loaded in Israeli ports between 2018-2048 according to main types of cargo:
Containers (Tons, TEU, Number of containers).
Bulk cargo (Clinker, plaster, metal slags)
Cement (cement bags and in bulk)
Grains (bulk and Dagon terminal)
Metals
General cargo (net)

## Slide 4: Main Stages of the Demand Prediction
Predicting demographic developments (population, labor force)
Forecasting Gross Domestic Product using a supply-side model (employees, capital, total factor productivity).
Forecasting industries output, import, and export according to a detailed macro-economic model (for 21 industries).
Estimating the demand according to type of cargo:
  Containers: according to a statistical model that connects value of import (in constant dollars) with volume of cargo unloaded.
  Cement, clinker, and plaster: according to a construction forecasting model.
  Grains and grain products: according to agriculture and food demand models.
Estimating exports loaded, according to type of cargo.

## Slide 5: Sources for Cargo Forecast Data
Data for cargo by type has been received from the Israel Ports Company.
Data for value of import and export by items in current and constant prices are based on CBS data (Foreign Trade Statistics monthly).
Export and import data in current dollars were converted to constant prices (2010 US dollars) by price indexes per each item.
Data for GDP, export and import in constant prices are base on CBS publications. Data are presented in constant 2017 New Israeli Shekels.
Population forecasts are based on CBS forecasts: “Populations forecast up to 2065” (published May 2018).
Macro forecasts (GDP, demand, construction and agriculture industries) are based on the Macro-Analytics group of macro-economic models.
Cargo unloaded and loaded are based on a model built especially for this project.
Construction material, grain and product forecasts are based on a model built especially for this project.

## Slide 6
The population of Israel will reach 15 million by 2048.
Population growth rate will decrease gradually to 1.7%.
Percentage of the population over age 65 will rise from 11% to 15% (aging of the population)
Percentage of the core working age population (25 to 64 years) will decrease from 45% to 42%.
Labor force participation rate will decrease gradually to 62.5%
Forecast assumptions:
  Partially bridging the gap in participation rates between populations (Ultra-Orthodox, Arab, Jewish).
  Increase in retirement age for women.
Demographic Forecast - Main Results

## Slide 7: Demographic Forecast, Population
 | 2018 | 2028 | 2038 | 2048 | 2019-2028 | 2029-2038 | 2039-2048
 | level, thousands |  |  |  | average annual percent change |  | 
Total population | 8,870 | 10,646 | 12,663 | 15,024 | 1.84% | 1.75% | 1.72%
Ages 0-14 | 2,513 | 3,010 | 3,507 | 4,194 | 1.8% | 1.5% | 1.8%
Ages 15-24 | 1,337 | 1,635 | 1,979 | 2,283 | 2.0% | 1.9% | 1.4%
Ages 25-64 | 3,989 | 4,622 | 5,416 | 6,328 | 1.5% | 1.6% | 1.6%
Ages 65+ | 1,030 | 1,380 | 1,762 | 2,218 | 3.0% | 2.5% | 2.3%
Source: CBS, Population Forecast, May 2018

## Slide 8: Demographic Forecast, Labor Force Participation Rate
% of labor force | 2018 | 2028 | 2038 | 2048
Total | 63.8% | 63.1% | 63.0% | 62.4%
Ages 15 through 24 | 54.5% | 55.6% | 55.6% | 54.5%
Ages 25 through 64 | 78.7% | 79.2% | 80.1% | 80.6%
Ages 65 and over | 17.8% | 18.2% | 18.5% | 18.8%
Source: population and demographic model.

## Slide 9: Macro Economic Forecast, Supply Side
 | 2018 | 2028 | 2038 | 2048 | 2019-2028 | 2029-2038 | 2039-2048
 | level |  |  |  | average annual percent change |  | 
Population, thousands | 8,870 | 10,646 | 12,663 | 15,024 | 1.8% | 1.8% | 1.7%
GDP, billions 2017 NIS | 1,315 | 1,803 | 2,488 | 3,405 | 3.2% | 3.3% | 3.2%
GDP per capita, thousands 2017 NIS | 148 | 169 | 196 | 226 | 1.3% | 1.5% | 1.4%
Employees, thousands | 3,893 | 4,608 | 5,521 | 6,545 | 1.7% | 1.8% | 1.7%
GDP per employee, thousands 2017 NIS | 337 | 390 | 450 | 519 | 1.5% | 1.4% | 1.4%

## Slide 10: Macro Economic Forecast, Demand Side
 | 2019-2028 | 2029-2038 | 2039-2048 | 2018 | 2028 | 2038 | 2048
 | average annual percent change |  |  | Share in GDP |  |  | 
GDP | 3.20% | 3.28% | 3.19% | 100% | 100% | 100% | 100%
Private Consumption | 3.6% | 3.5% | 3.4% | 55% | 57% | 59% | 60%
Public Consumption | 2.7% | 2.7% | 2.7% | 22% | 21% | 20% | 19%
Investment, total | 3.2% | 3.3% | 3.2% | 21% | 21% | 21% | 21%
Exports, Goods and Services | 3.8% | 3.8% | 3.7% | 31% | 33% | 34% | 36%
Imports, Goods and Services | 4.2% | 3.8% | 3.6% | 29% | 32% | 33% | 35%

## Slide 11: Container Imports – Unloaded (not including empty containers or trans-shipments)

## Slide 12: Container Imports – Unloaded The Model
The purpose of the model is to translate the value of goods (determined with the macro-economy model) into container traffic.
We use an econometric model. We regressed the weight unloaded on value of import in constant dollars.
69 series of import items (from foreign trade data) were aggregated into 3 main series.
The criteria of the aggregations:
  Economic use of import (consumer, raw materials)
  Achieving the best fit (R-square)
We omitted items that are non-relevant to container shipment or that were insignificant to the power of statistical explanation.

## Slide 13: Container Imports – Unloaded The Model
X1 – Import items of non-durable consumer goods.
X2 – Import items of durable consumer goods.
X3 – Import items of raw materials.
Y – Container weight, unloaded (in tonnage)

## Slide 14: Explanatory Variables
 | 2017 Millions 2010 US$ | Out of total import | % change 2008-2017
Consumer – Durable Goods. (X1) | 4,677 | 9% | 7.0%
Consumer – Non- Durable Goods (X2) | 5,311 | 10% | 4.4%
Raw Materials (X3) | 21,829 | 41% | 2.9%
Total (X1+X2+X3) | 31,817 | 60% | 3.7%

## Slide 15: Container Imports, Unloaded Actual vs Predicted
Chart: weight, thousands Tons
| 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017
Actual | 7446.2196 | 8287.3855 | 8639.6954 | 7920.9449 | 9007.4166 | 9597.3193 | 9838.9134 | 10404.8567 | 10755.7386 | 11523.8187 | 12705.6739 | 13236.2334
Predicted | 7373.9231 | 7971.9166 | 8648.8282 | 8016.1027 | 8934.1748 | 9532.6348 | 10214.5797 | 10489.7394 | 11172.6543 | 11646.0979 | 12413.148 | 12950.4166

## Slide 16: Container Imports, Unloaded – Forecast
Chart: weight, thousands Tons
| 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048
Predicted | 7373.9231 | 7971.9166 | 8648.8282 | 8016.1027 | 8934.1748 | 9532.6348 | 10214.5797 | 10489.7394 | 11172.6543 | 11646.0979 | 12413.148 | 12950.4166 | 13847.365 | 14515.0551 | 15193.9235 | 15904.9906 | 16640.9349 | 17404.118 | 18192.5229 | 19006.5708 | 19832.8551 | 20691.5692 | 21580.748 | 22506.227 | 23460.4549 | 24452.4395 | 25488.0991 | 26552.9545 | 27653.5903 | 28786.4576 | 29906.1732 | 31065.4087 | 32259.1149 | 33495.9586 | 34768.6134 | 36082.3949 | 37447.5227 | 38864.3402 | 40321.6799 | 41826.8976 | 43384.1546 | 44991.5656 | 46648.44
Containers unloaded are expected to increase by 3.6 times by 2048.

## Slide 17: Container Imports, Unloaded – Forecast
 | 2018 | 2028 | 2038 | 2048 | 2019-2028 | 2029-2038 | 2039-2048
 | Level, billions 2017 NIS |  |  |  | average annual percent change |  | 
GDP | 1,314.9 | 1,802.5 | 2,488.1 | 3,405.0 | 3.2% | 3.3% | 3.2%
Total Import (goods and services) | 350.5 | 518.1 | 751.0 | 1,065.8 | 4.0% | 3.8% | 3.6%
 | Level, Millions 2010 US $ |  |  |  | average annual percent change |  | 
Import, Consumer – Durable | 5,025 | 8,046 | 12,472 | 18,447 | 4.8% | 4.5% | 4.0%
Import, Consumer – Non- durable | 6,600 | 14,400 | 25,600 | 40,179 | 8.1% | 5.9% | 4.6%
Import, Raw Materials | 22,750 | 30,751 | 41,237 | 54,897 | 3.1% | 3.0% | 2.9%
Containers, Unloaded Thousands Tons | 13,847 | 21,196 | 31,730 | 45,803 | 4.3% | 4.1% | 3.7%

## Slide 18: GDP, Import and Containers Unloaded Index 2018=100
Chart: 
| 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048
GDP | 100 | 103.1044 | 106.259 | 109.6307 | 113.1415 | 116.7996 | 120.5789 | 124.475 | 128.5158 | 132.7245 | 137.079 | 141.6178 | 146.2775 | 151.1209 | 156.1858 | 161.3596 | 166.6869 | 172.1379 | 177.6566 | 183.3627 | 189.2169 | 195.2763 | 201.4864 | 207.8806 | 214.5248 | 221.4166 | 228.4766 | 235.7508 | 243.2629 | 250.9966 | 258.9436
Import | 100 | 103.9623 | 108.004 | 112.2465 | 116.6392 | 121.1917 | 125.8884 | 130.7291 | 135.8138 | 141.0906 | 146.5462 | 152.2121 | 158.044 | 164.0915 | 170.3862 | 176.8459 | 183.5067 | 190.3482 | 197.3219 | 204.529 | 211.9418 | 219.6072 | 227.4855 | 235.6052 | 244.0211 | 252.7346 | 261.6857 | 270.9135 | 280.4402 | 290.2554 | 298.6301
Containers Unloaded | 100 | 104.5452 | 109.1547 | 113.9778 | 118.9603 | 124.1175 | 129.4338 | 134.911 | 140.7405 | 146.7987 | 153.0712 | 159.5992 | 166.329 | 173.3242 | 180.6266 | 188.1334 | 195.8913 | 203.875 | 212.0157 | 220.4506 | 229.1446 | 238.1599 | 247.4451 | 257.0387 | 267.0143 | 277.3752 | 288.0425 | 299.0696 | 310.4871 | 322.2822 | 330.7691
Import growth rate is expected to be higher than GDP growth rate due to a continuation of the specialization process. Growth rate in containers unloaded will be higher than growth rate of imports due to a continuing increase in the import of durable and non-durable consumers goods.

## Slide 19: Container Imports, Unloaded – Forecast
 | 2018 | 2028 | 2038 | 2048 | 2019-2028 | 2029-2038 | 2039-2048
 | level |  |  |  | average annual percent change |  | 
Containers, Unloaded, Thousands Tons | 13,847 | 21,196 | 31,730 | 45,803 | 4.3% | 4.1% | 3.7%
Containers, Unloaded Thousands units, 20 ft. | 370 | 514 | 756 | 1,088 | 3.4% | 3.9% | 3.7%
Containers, Unloaded Thousands units, 40 ft. | 449 | 743 | 1,128 | 1,631 | 5.2% | 4.3% | 3.8%
% of 40 ft. containers out of total number of units | 55% | 59% | 60% | 60% | 0.8% | 0.1% | 0.0%
Containers, Unloaded, Thousands TEU | 1,267 | 2,001 | 3,012 | 4,351 | 4.7% | 4.2% | 3.7%

## Slide 20: Container Imports – Unloaded Summary of Forecast
Growth potential of 3.2% per year.
Import of goods and services is expected to grow by 3.8% per year due to a continuation of the specialization process.
Value of goods in containers is expected to grow by 4.1% per year due to excess growth in durable and non-durable consumer goods.
Containers loaded in terms of weight (tonnage) are expected to grow by 4.1% per year.
Containers loaded in terms of TEU are expected to grow by 4.2% due to a continuation of growth in the share of the 40 ft. containers.

## Slide 21: Container Exports – Loaded (not including empty containers or trans-shipment)

## Slide 22: Container Exports – Loaded The Model
Identifies the value in constant price (volume index) of exports from Israel.
Translates the value of goods exported from Israel into container trade using a statistical model.
22 series of industrial and agricultural export (from foreign trade data) were aggregated into 3 main series using an econometric model.
The criterion was to achieve the best fit (R-square).
We omitted export items that are non-relevant to container shipment (such as electronic components, medicines) or that were statistically insignificant.

## Slide 23: Container Exports – Loaded
X1 – Export of electronic, optical and medical products.
X2 – Export of traditional industrial products.
X3 – Export of agricultural products.
Y – Container weight loaded (in tons)

## Slide 24: Explanatory Variables
 | 2017 Mil’ 2010 US $ | Out of total | % change 2008-2017
Export of electronic, optical and medical products. (X1) | 8,422 | 17% | 3.1%
Traditional Industrial Exports (X2) | 12,932 | 27% | 3.0%
Export of agricultural products(X3) | 1,165 | 2% | 0.2%
Total (X1+X2+X3) | 22,519 | 47% | 2.8%

## Slide 25: Container Imports, Unloaded Actual vs Predicted
Chart: weight, thousands Tons
| 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015
Actual | 3888.4841 | 4305.1981 | 4392.9523 | 5053.2516 | 5101.0087 | 4636.5055 | 5180.7765 | 5300.7692 | 5395.4652 | 5437.6202 | 5432.5933 | 5045.612
Predicted | 3983.4628 | 4180.4951 | 4718.0022 | 5188.2087 | 5298.0176 | 4510.4162 | 5142.2163 | 5416.3561 | 5345.2988 | 5141.1571 | 5264.6549 | 4981.951

## Slide 26: Container Exports, Loaded – Forecast
History Projections
2017
Chart: weight, thousands Tons
| 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048
משקל חזוי | 3983.4628 | 4180.4951 | 4718.0022 | 5188.2087 | 5298.0176 | 4510.4162 | 5142.2163 | 5416.3561 | 5345.2988 | 5141.1571 | 5264.6549 | 4981.951 | 5529.0439 | 5544.5557 | 5772.5243 | 5968.8862 | 6171.119 | 6379.3117 | 6593.5535 | 6813.9336 | 7040.5411 | 7273.4648 | 7512.7932 | 7758.6141 | 8011.0149 | 8270.0821 | 8535.9014 | 8808.5579 | 9088.1352 | 9374.7161 | 9668.3823 | 9969.2141 | 10277.2904 | 10592.6891 | 10915.4863 | 11245.7566 | 11583.5732 | 11929.0076 | 12282.1295 | 12643.007 | 13011.7063 | 13388.292 | 13772.8265 | 14165.3705 | 14565.9825
Containers loaded are expected to increase by 2.5 times by 2048.

## Slide 27: Container Exports, Loaded – Forecast
 | 2018 | 2028 | 2038 | 2048 | 2019-2028 | 2029-2038 | 2039-2048
 | Level, billions, 2017 NIS |  |  |  | average annual percent change |  | 
GDP | 1,314.9 | 1,802.5 | 2,488.1 | 3,405.0 | 3.2% | 3.3% | 3.2%
Export | 376.9 | 547.3 | 791.2 | 1,126.9 | 3.8% | 3.8% | 3.6%
 | Level, millions 2010 US $ |  |  |  | average annual percent change |  | 
Electronic Exports | 9,349 | 13,610 | 19,134 | 26,061 | 3.8% | 3.5% | 3.1%
Traditional Exports | 14,036 | 18,322 | 23,944 | 31,113 | 2.7% | 2.7% | 2.7%
Agricultural Exports | 1,176 | 1,274 | 1,379 | 1,494 | 0.8% | 0.8% | 0.8%
Containers, Loaded, Thousands Tons | 5,773 | 8,011 | 10,915 | 14,566 | 3.3% | 3.1% | 2.9%

## Slide 28: GDP, Export and Containers Loaded Index 2018=100
Chart: 
| 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048
GDP | 100 | 103.1044 | 106.259 | 109.6307 | 113.1415 | 116.7996 | 120.5789 | 124.475 | 128.5158 | 132.7245 | 137.079 | 141.6178 | 146.2775 | 151.1209 | 156.1858 | 161.3596 | 166.6869 | 172.1379 | 177.6566 | 183.3627 | 189.2169 | 195.2763 | 201.4864 | 207.8806 | 214.5248 | 221.4166 | 228.4766 | 235.7508 | 243.2629 | 250.9966 | 258.9436
Export | 100 | 103.8208 | 107.7912 | 111.9153 | 116.1977 | 120.6428 | 125.2551 | 130.0393 | 134.9999 | 140.1417 | 145.4693 | 150.9876 | 156.7014 | 162.6155 | 168.7349 | 175.0643 | 181.6089 | 188.3735 | 195.3631 | 202.5828 | 210.0374 | 217.7321 | 225.6719 | 233.8616 | 242.3064 | 251.0112 | 259.9809 | 269.2206 | 278.7351 | 288.5294 | 298.6081
Containers loaded | 100 | 103.4017 | 106.905 | 110.5116 | 114.2231 | 118.0408 | 121.9664 | 126.0015 | 130.1475 | 134.4059 | 138.7784 | 143.2663 | 147.8712 | 152.5946 | 157.4378 | 162.4024 | 167.4897 | 172.7011 | 178.0381 | 183.5019 | 189.0938 | 194.8152 | 200.6674 | 206.6515 | 212.7688 | 219.0204 | 225.4076 | 231.9313 | 238.5928 | 245.393 | 252.333
Export growth rate is expected to be higher than GDP growth rate as a result of continuation of the specialization process. The growth rate of containers loaded is predicted to be lower than GDP growth rate due to continued increase in the proportion of export services at the expense of the industrial export.

## Slide 29: Container Export, Loaded – Forecast
 | 2018 | 2028 | 2038 | 2048 | 2019-2028 | 2029-2038 | 2039-2048
 | level |  |  |  | average annual percent change |  | 
Containers, Loaded Thousands Tons | 5,773 | 8,011 | 10,915 | 14,566 | 3.3% | 3.1% | 2.9%
Containers, Loaded Thousands units, 20 ft, | 128 | 156 | 201 | 264 | 2.0% | 2.6% | 2.7%
Containers, Loaded Thousands units, 40 ft. | 216 | 323 | 453 | 609 | 4.1% | 3.4% | 3.0%
% of 40 ft. containers out of total number of units | 63% | 67% | 69% | 70% | 0.7% | 0.3% | 0.1%
Containers, Loaded, Thousands TEU | 560 | 802 | 1,107 | 1,482 | 3.7% | 3.3% | 3.0%

## Slide 30: Loading of: Cement - Bulk & General Cargo Clinker Plaster

## Slide 31: Demand for construction materials – the model
Cement demand forecast is based on an external model of the construction industry divided into housing investment, non-housing investment and infrastructure investment.
Cement demand forecast for the Palestinian Authority and Gaza is based on population forecast and on per capita cement intensity forecasts to these areas.
Over the past years cement import via Ashdod and Haifa ports grew rapidly.
Local production is expected to grow at a slower pace. We assume 1% growth rate up to 2028, a lower growth rate compared to demand growth, such that import share will continue to grow.
As of 2009, the rate of increase in domestic production will be identical to local demand growth. Surplus demand from the Palestinian Authority and Gaza will be provided by imports.

## Slide 32: Construction Industry Forecasts, 2018-2048
 | 2018 | 2028 | 2038 | 2048 | 2019-2028 | 2029-2038 | 2039-2048
Investment | Level, millions 2017 NIS |  |  |  | average annual percent change |  | 
Residential Building | 77,263 | 112,696 | 126,491 | 133,795 | 3.8% | 1.2% | 0.6%
Commercial Building | 28,313 | 34,261 | 45,378 | 58,830 | 1.9% | 2.9% | 2.6%
Infrastructure | 26,876 | 35,996 | 51,526 | 70,587 | 3.0% | 3.7% | 3.2%
 | Units, Area, thousands of sqm |  |  |  | average annual percent change |  | 
Residential Building Starts (Units) | 43,729 | 78,129 | 86,573 | 90,827 | 6.0% | 1.0% | 0.5%
Residential Building Starts ('m m2) | 7,827 | 14,165 | 16,072 | 17,257 | 6.1% | 1.3% | 0.7%
Commercial Building Starts ('m m2) | 3,050 | 3,559 | 4,516 | 5,614 | 1.6% | 2.4% | 2.2%

## Slide 33: Cement Import Forecasts, 2018-2048, in Thousands of Tons
 | 2018 | 2028 | 2038 | 2048 | 2019-2028 | 2029-2038 | 2039-2048
Thousands Tons | level |  |  |  | average annual percent change |  | 
Local (Israel) Demand | 6,930 | 8,494 | 9,826 | 11,199 | 2.1% | 1.5% | 1.3%
Palestinian Authority and Gaza Demand | 2,678 | 3,663 | 4,553 | 5,525 | 3.2% | 2.2% | 2.0%
Total Cement Demand | 9,608 | 12,157 | 14,379 | 16,724 | 2.4% | 1.7% | 1.5%
Local Production | 6,471 | 7,148 | 8,269 | 9,425 | 1.0% | 1.5% | 1.3%
Import through Ports | 2,142 | 3,910 | 4,896 | 5,959 | 6.2% | 2.3% | 2.0%
Land Imports | 995 | 1,099 | 1,214 | 1,341 | 1.0% | 1.0% | 1.0%
Source:

## Slide 34: Loading of: Grains and Grain product

## Slide 35: Grains and grain product demand - the model
Grains and grain product forecasts are based on an external model of agricultural and food sectors.
The model links the demand for grains and the various uses of grains:
  Grains for animal feed.
  Grains for wheat.
  Beans for oil production.
Animal feed grain demand is determined by per capita consumption of meat & poultry and different grains’ utilization factor.
Per capita demand elasticity of meat will gradually decline to zero from the high rates of the last decade (1-1.5).
Switching to meat substitutes (vegetarianism) may accelerate this trend.

## Slide 36
 | 2018 | 2048 | average annual percent change, 2019-2048
Beans, Thousands Tons | 541 | 614 | 0.4%
Grains for wheat, Thousands Tons | 1,059 | 1,451 | 1.1%
Grains for animal feed, Thousands Tons | 4,090 | 7,544 | 2.1%
Grains and grain products, total | 5,691 | 9,610 | 1.8%
Grains and grain product demand